## Slide 1: Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
Jiachen Lu
Jiachen Lu

## Slide 2
How many of you have heard of wireless signals (WiFi, Bluetooth, mmWave)?
How many of you have heard of mmWave (5G, 6G, Next-Gen WiFi)?
How many of you have prior knowledge on mmWave sensing (Imaging, FMCW, AoA)?
How many of you have prior research experience in mmWave sensing?
No prior mmWave experience necessary!
Notes: After 2nd: in what context have you heard it?

## Slide 3
There have been incredible advances in computer vision

## Slide 4
There have been incredible advances in computer vision

## Slide 5
There have been incredible advances in computer vision

## Slide 6
There have been incredible advances in computer vision
What is inside the boxes?
What if we could build imaging & perception systems
which can see hidden objects?

## Slide 7
camera view static (gone), robot scanning (v fast or only partial), - camera view gets bigger, open box - blur to spoon gets smaller
Add baseline
Add ours
Spin all 3
High-Accuracy Non-Line-of-Sight 3D Reconstruction has Many Applications
Shipping & Logistics
Robotics
Augmented Reality

## Slide 8
Wireless signals can travel through everyday occlusions

## Slide 9
Wireless signals can travel through everyday occlusions
Millimeter-Wave (mmWave)
5G, 6G, Next-Gen WiFi

## Slide 10
Wireless signals can travel through everyday occlusions
Millimeter-Wave (mmWave)
5G, 6G, Next-Gen WiFi
Cardboard
Plastic
Fabric
Fog
Smoke

## Slide 11
Wireless signals can travel through everyday occlusions
We can use them to image, reconstruct, & perceive the hidden environment

## Slide 12
Wireless signals can travel through everyday occlusions
We can use them to image, reconstruct, & perceive the hidden environment

## Slide 13
Wireless signals can travel through everyday occlusions
We can use them to image, reconstruct, & perceive the hidden environment

## Slide 14
Wireless signals can travel through everyday occlusions
We can use them to image, reconstruct, & perceive the hidden environment

## Slide 15
Is mmWave imaging & reconstruction a solved problem?
Top View
Side View

## Slide 16
Is mmWave imaging & reconstruction a solved problem?
Top View
Side View
Missing Parts
Large Power Spread
High Noise

## Slide 17
What are most common mmWave imaging research domains?
Scale
Complexity
Object Level
Human Level
Scene Level
Presence Detection or Coarse Imaging
3D
Reconstruction
Obstacle Detection: Widely Deployed
3D Skeletons & Meshes
+ Gesture Recognition
+ Vital Monitoring
High-Fidelity Reconstruction
+ Segmentation
+ Material property estimation
+SLAM
Object Bounding Boxes
Object Imaging
+ Classification
+Segmentation
Human Detection

## Slide 18
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 19
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 20: mmWave 101: The basics of mmWave imaging

## Slide 21
How does mmWave compare to other through-occlusion modalities?
XRay
Thermal
Ultrasound
Reflected Lasers
Unsafe for
extended exposure
Requires heat
Cannot see through walls
Requires gel to
minimize mismatch
Cannot travel
through occlusions
mmWave is safe, operates through occlusions,
and can image everyday objects

## Slide 22
What is a mmWave sensor?
“Radar”
Antenna
Array

## Slide 23
What is a mmWave sensor?
“Radar”
Antenna
Array
A mmWave radar transmits and receives signals
It does not directly capture an image

## Slide 24
How do we measure a mmWave Image?
Range (r)
Angle
(ϴ)
Estimate the power reflected from this point (range, angle) in space
Image
Single Point Reflector
Each pixel is an approximation of power reflected from that point

## Slide 25
How do we measure a mmWave Image?
Range (r)
Angle
(ϴ)
Estimate the power reflected from this point (range, angle) in space
Image
Single Point Reflector

## Slide 26
How do we measure a mmWave Image?
Range (r)
Angle
(ϴ)
Estimate the power reflected from this point (range, angle) in space

## Slide 27
How do we measure a mmWave Image?
Estimate the power reflected from this point (range, angle) in space

## Slide 28
How do we measure a mmWave Image?
Estimate the power reflected from this point (range, angle) in space
How do we estimate range with mmWave signals?
How do we estimate angle with mmWave signals?

## Slide 29
How do we measure a mmWave Image?
Estimate the power reflected from this point (range, angle) in space
How do we estimate range with mmWave signals?
How do we estimate angle with mmWave signals?

## Slide 30
How do we estimate range with mmWave signals?
Measure time it takes signal to travel to object and back
“Time of Flight”
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 31
How do we estimate range with mmWave signals?
Measure time it takes signal to travel to object and back
“Time of Flight”
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 32
How do we estimate range with mmWave signals?
Measure time it takes signal to travel to object and back
“Time of Flight”
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 33
How do we estimate range with mmWave signals?
Measure time it takes signal to travel to object and back
“Time of Flight”
Range = Speed of Light x Time of Flight
r = c x τ
Measuring time of flight directly is very difficult
> $10k
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 34
How do we estimate range with mmWave signals?
Frequency Modulated Continuous Wave (FMCW)
Create a relationship between time of flight and frequency
Time
Amplitude
Time
Frequency
Transmit
Transmit
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 35
How do we estimate range with mmWave signals?
Frequency Modulated Continuous Wave (FMCW)
Create a relationship between time of flight and frequency
Time
Amplitude
Time
Frequency
Transmit
Transmit
Receive
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 36
How do we estimate range with mmWave signals?
Frequency Modulated Continuous Wave (FMCW)
Create a relationship between time of flight and frequency
Time
Amplitude
Time
Frequency
Transmit
Transmit
Receive
Receive
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 37
How do we estimate range with mmWave signals?
Frequency Modulated Continuous Wave (FMCW)
Create a relationship between time of flight and frequency
Time
Frequency
Transmit
Receive
τ
Δf
Slope (k)
Slope = Difference in Frequency / Time of Flight
k = Δf / τ
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 38
How do we estimate range with mmWave signals?
Frequency Modulated Continuous Wave (FMCW)
Create a relationship between time of flight and frequency
Time
Frequency
Transmit
Receive
τ
Δf
Slope (k)
Slope = Difference in Frequency / Time of Flight
k = Δf / τ
Difference in Frequency
Signal with frequency Δf
Time
Mixer
Analog Circuit Component
Multiplies Two Signals
Amplitude
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 39
How do we estimate range with mmWave signals?
Frequency Modulated Continuous Wave (FMCW)
Create a relationship between time of flight and frequency
Time
Frequency
Transmit
Receive
τ
Δf
Slope (k)
Slope = Difference in Frequency / Time of Flight
k = Δf / τ
Difference in Frequency
Signal with frequency Δf
Time
Mixer
Analog Circuit Component
Multiplies Two Signals
Amplitude
Notes: This is equalivent to trying to find out how far away a light source is based on delay between turning it on and seeing it in your video camera

## Slide 40
How do we estimate range with mmWave signals?
Frequency Modulated Continuous Wave (FMCW)
Create a relationship between time of flight and frequency
Time
Frequency
Transmit
Receive
τ
Δf
Slope (k)
Slope = Difference in Frequency / Time of Flight
k = Δf / τ
Difference in Frequency
Signal with frequency Δf
Time
Mixer
Analog Circuit Component
Multiplies Two Signals
We need to find Δf to find range
Amplitude

## Slide 41
How do we estimate range with mmWave signals?
Frequency Modulated Continuous Wave (FMCW)
Create a relationship between time of flight and frequency
Time
s(t) = cos(2 π Δf t + 2 π f0 τ)
s(t) = cos(2 π k τ t + 2 π f0 τ)
s(t) = e j 2 π k t r /c + j 2 π f0 r / c
We need to find Δf to find range
Amplitude
Fourier Transform
Frequency
Amplitude
s(t) = cos(2 π k r t / c + 2 π f0 r / c)

## Slide 42
How do we estimate range with mmWave signals?
Time
Amplitude
Fourier
Transform
Frequency
Amplitude
Δf
k τ
k r / c
Time
Frequency
Transmit
Receive
τ
Δf
Slope (k)
Mixer
Time
Amplitude
Transmit
Receive

## Slide 43
How do we measure a mmWave Image?
Estimate the power reflected from this point (range, angle) in space
How do we estimate range with mmWave signals?
How do we estimate angle with mmWave signals?
Time
Amplitude
Fourier
Transform
Frequency
Amplitude
Δf
k τ
k r / c
Time
Frequency
Transmit
Receive
τ
Δf
Slope (k)
Mixer
Time
Amplitude
Transmit
Receive

## Slide 45
How do we estimate angle with mmWave signals?

## Slide 46
How do we estimate angle with mmWave signals?
Compare difference between signal at two locations

## Slide 47
How do we estimate angle with mmWave signals?
Compare difference between signal at two locations

## Slide 48
How do we estimate angle with mmWave signals?
Compare difference between signal at two locations

## Slide 49
How do we estimate angle with mmWave signals?
Compare difference between signal at two locations

## Slide 50
How do we estimate angle with mmWave signals?
Far Field Assumption
Reflector is far away that the lines become parallel

## Slide 51
How do we estimate angle with mmWave signals?
Far Field Assumption
Reflector is far away that the lines become parallel

## Slide 52
How do we estimate angle with mmWave signals?

## Slide 53
How do we estimate angle with mmWave signals?

## Slide 54
How do we estimate angle with mmWave signals?
Signal travels further to right antenna
Signal travels equal distances
Signal travels further to left antenna
Extra
Distance
Angle
(ϴ)
Extra
Distance

## Slide 55
How do we estimate angle with mmWave signals?
Extra
Distance
Angle
(ϴ)

## Slide 56
How do we estimate angle with mmWave signals?
Angle
(ϴ)
Fourier Transform
Angle
Amplitude

## Slide 57
How do we measure a mmWave Image?
Estimate the power reflected from this point (range, angle) in space
How do we estimate range with mmWave signals?
How do we estimate angle with mmWave signals?
Time
Amplitude
Fourier
Transform
Frequency
Amplitude
Δf
k τ
k r / c
Time
Frequency
Transmit
Receive
τ
Δf
Slope (k)
Mixer
Time
Amplitude
Transmit
Receive
Fourier Transform
Amplitude
Angle

## Slide 58
Estimate the power reflected from this point (range, angle) in space
range
angle

## Slide 59
Estimate the power reflected from this point (range, angle) in space

## Slide 60
Extending from 2D to 3D
Notes: Are we done?
No wouldn’t have job

## Slide 61
Extending from 2D to 3D
Notes: Are we done?
No wouldn’t have job

## Slide 62
What are the challenges of mmWave?

## Slide 63
What are the challenges of mmWave?
Resolution of mmWave image is low compared to cameras

## Slide 64
What are the challenges of mmWave?
Resolution of mmWave image is low compared to cameras

## Slide 65
Resolution of mmWave image is low compared to cameras
Range Resolution
∝ Bandwidth
Range of frequencies
sent in FMCW
Horizontal Resolution
∝ Aperture
Distance from First to Last Antenna

## Slide 66
Resolution of mmWave image is low compared to cameras
Range Resolution
∝ Bandwidth
Range of frequencies
sent in FMCW
Horizontal Resolution
∝ Aperture
Distance from First to Last Antenna

## Slide 67
Resolution of mmWave image is low compared to cameras
Range Resolution
∝ Bandwidth
Range of frequencies
sent in FMCW
Limited by
government
regulations
Horizontal Resolution
∝ Aperture
Distance from First to Last Antenna
Synthetic Aperture Radar
Move radar to new locations
If object isn’t moving, equivalent to adding more antennas on the radar
Can increase horizontal resolution
Horizontal resolution can be increased by taking more measurements
Range resolution cannot be increased
Notes: Similar to how in a camera, pixels define resolution

## Slide 68
Resolution of mmWave image is low compared to cameras
Top View
Side View
Large Power Spread

## Slide 69
What are the challenges of mmWave?
Resolution of mmWave image is low compared to cameras
Coverage of mmWave image is limited by specularity

## Slide 70
Coverage of mmWave image is limited by specularity
Object Surface
No Signal Received
Signal Received

## Slide 71
Coverage of mmWave image is limited by specularity
Object Surface

## Slide 72
Coverage of mmWave image is limited by specularity
Object Surface
Portions of Object Unseen

## Slide 73
What are the challenges of mmWave?
Resolution of mmWave image is low compared to cameras
Coverage of mmWave image is limited by specularity
mmWave signals suffer high noise & do not provide color information
We will be discussing several state-of-the-art methods to overcome these challenges

## Slide 74
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 75
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 76: Non-Line-of-Sight 3D Object Reconstruction via mmWave Surface Normal Estimation
Laura Dodds, Tara Boroushaki, Kaichen Zhou, Fadel Adib
Cartesian
Systems

## Slide 77: How can we go from 3D imaging to 3D reconstruction?

## Slide 78
How can we go from 3D imaging to 3D reconstruction?

## Slide 79
Range
Resolution
*
How can we go from 3D imaging to 3D reconstruction?
* Mobicom ‘24
Naïve Solution: Select every voxel above a power threshold

## Slide 80
How can we go from 3D imaging to 3D reconstruction?
* Mobicom ‘24
*

## Slide 81
camera view static (gone), robot scanning (v fast or only partial), - camera view gets bigger, open box - blur to spoon gets smaller
Add baseline
Add ours
Spin all 3
High-Accuracy Non-Line-of-Sight 3D Reconstruction has Many Applications
Robotics
Augmented Reality
Shipping & Logistics

## Slide 82
mmNorm
A new & highly-accurate method for 3D object reconstruction leveraging an entirely first-principles based approach
Introduces techniques for mmWave Surface Normal Estimation and mmWave Structural Isosurface Optimization
Achieves a qualitative leap in mmWave reconstruction over state-of-the-art methods

## Slide 83: How do existing methods perform 3D reconstruction?
Airplane with
Radar
Synthetic Aperture
Produce a 3D SAR Image
Range
Azimuth
Elevation
2D Synthetic Aperture
Generate 3D point cloud
TomoSAR, 1997
Notes: Now before I tell you how mmNorm works, it is helpful for me to first explain how existing methods perform 3d reconstruction. Now for the most part, we as a community have been performing 3D reconstruction in the same way for decades. For example, it startwed when we wanted to reconstruct large scale scenese such as this mountain scene. So we as a community mounted a radar onto an airplane or satellite, and have the airplane fly over the scene, continuously collecting measurements to produce a synthetic aperture. Then, we can have the same airplane fly over the scene multiple times to expand our synthetic aperture into a 2D synthetic aperture.
This allows us to measure the range, azimuth, and elevation to different reflectors in the scene. With this, we can produce a 3D SAR image, and use this to generate a 3D point cloud.

## Slide 84
Object to
Reconstruct
How do existing methods perform 3D reconstruction?
Reconstruction quality is limited by SAR resolution (i.e., bandwidth)
Produce a 3D SAR Image
Generate 3D point cloud
IMWUT ‘23, Mobicom ‘24
Notes: Now when we as a community wanted to move from these large scale scenes to much smaller objects, we applied almost the exact same approach. For example, to reconstruct this mug here, past work has attached a radar to a robot or linear stage. The robot then moves the radar, again collecting a 2D synthetic aperture. Again, we can produce a 3D SAR image, and use this to generate a 3D point cloud.
But this time, there is a problem. Unlike before, where we were reconstructing massive mountain scenes, we are now trying to reconstruct a tiny mug. This means that now our reconstruction quality is severely limited by our SAR resolution, which in this case is limited by our commercially available bandwidth.

## Slide 85
How do existing methods perform 3D reconstruction?
Reconstruction quality is limited by SAR resolution (i.e., bandwidth)
Real-World
3D Point Cloud

## Slide 86
How do existing methods perform 3D reconstruction?
Points are spread due to limited resolution
First-Principles Methods
Machine-Learning Methods
Requires Significant Training Data
Typically operate on very small subset of objects
Reconstruction quality is limited by SAR resolution (i.e., bandwidth)
3D Model
We need a fundamentally new approach for
mmWave 3D object reconstruction
Our Idea: Directly estimate the curvature of the object
CVPR ‘20, Mobicom ‘24

## Slide 87
Surface
Normal
Vector
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors

## Slide 88
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors

## Slide 89
Synthetic
Aperture
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors
Surface Normal Vector Field

## Slide 90
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors
1. Normal Field Estimation

## Slide 91
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors
1. Normal Field Estimation
2. Multiple Valid Surfaces

## Slide 92
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors
1. Normal Field Estimation
2. Multiple Valid Surfaces
3. Single Unifying
Function
Isosurface: Surface of constant value
Relative Signed Distance Function
4. Isosurface
Optimization

## Slide 93
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors
1. Normal Field Estimation
2. Multiple Valid Surfaces
3. Single Unifying
Function
4. Isosurface
Optimization
Isosurface: Surface of constant value
Relative Signed Distance Function
Final Surface Estimate

## Slide 94
Synthetic
Aperture
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors

## Slide 95
Synthetic
Aperture
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors

## Slide 96
Synthetic
Aperture
Object Surface
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors

## Slide 97
Synthetic
Aperture
mmWave signals experience primarily specular reflections
Object Surface
No Signal Received
Signal Received

## Slide 98
At a given voxel, what direction is the surface normal?
Voxel
Possible Surface Normals
Due to specularity, these normal do not produce reflections towards the aperture
Lets say one of these antennas receive a reflection from this voxel

## Slide 99
At a given voxel, what direction is the surface normal?
Voxel
v1
v2
v3
v4
v5
v6
v7
Reflection amplitude acts as a vote

## Slide 100
At a given voxel, what direction is the surface normal?
v1
v2
v3
v4
v5
v6
v7
Reflection amplitude acts as a vote

## Slide 101
At a given voxel, what direction is the surface normal?
v1
v2
v3
v4
v5
v6
v7
Reflection amplitude acts as a vote
Example 1
Example 2

## Slide 102
At a given voxel, what direction is the surface normal?
v1
v2
v3
v4
v5
v6
v7
Reflection amplitude acts as a vote
Example 1
Example 2

## Slide 103
At a given voxel, what direction is the surface normal?
v1
v2
v3
v4
v5
v6
v7
Reflection amplitude acts as a vote
Example 1
Example 2
v1
v2
v3
v4
v5
v6
v7

## Slide 104
At a given voxel, what direction is the surface normal?
v1
v2
v3
v4
v5
v6
v7
Reflection amplitude acts as a vote
Example 1
Example 2
v1
v2
v3
v4
v5
v6
v7

## Slide 105
Weighted Sum
At a given voxel, what direction is the surface normal?
v1
v2
v3
v4
v5
v6
v7
Reflection amplitude acts as a vote
arriving from this voxel in SAR image

## Slide 106
Sum across
frequency
Received
signal
Expected
signal
Individual
Antenna
Value
mmWave
Voxel Value
Sum across
antennas
Individual
Antenna
Values
How do we compute the voting function?
Reflection amplitude acts as a vote
arriving from this voxel in SAR image

## Slide 107
Voting Function:
Reflection amplitude acts as a vote
arriving from this voxel in SAR image
Large Projection Magnitude
mmWave
Voxel
Value
Antenna 1 Value
Q
I
Antenna 2 Value
Small Projection Magnitude
We repeat this at every voxel in space to produce a normal vector field
How do we compute the voting function?

## Slide 108
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors
1. Normal Field Estimation
2. Multiple Valid Surfaces
3. Single Unifying
Function
4. Isosurface
Optimization
Isosurface: Surface of constant value
Relative Signed Distance Function
Final Surface Estimate

## Slide 109
How can we capture all ambiguous surfaces in one function?
0 at surface of object
Positive values
Negative values
Signed Distance Function
Normal Vector
Field
Relative Signed Distance Function
Computer Graphics
mmNorm
Normal Vector
Field
Unknown constant offset

## Slide 110
Positive values
Negative values
0 at surface of object
Signed Distance Function
Normal Vector
Field
Relative Signed Distance Function
Computer Graphics
mmNorm
Normal Vector
Field
How can we capture all ambiguous surfaces in one function?
Unknown constant offset

## Slide 111
Positive values
Negative values
0 at surface of object
Signed Distance Function
Normal Vector
Field
Relative Signed Distance Function
Computer Graphics
mmNorm
Normal Vector
Field
How can we capture all ambiguous surfaces in one function?
Unknown constant offset

## Slide 112
Positive values
Negative values
0 at surface of object
Signed Distance Function
Normal Vector
Field
Relative Signed Distance Function
Computer Graphics
mmNorm
Normal Vector
Field
How can we capture all ambiguous surfaces in one function?
Unknown constant offset

## Slide 113
Positive values
Negative values
Computer Graphics
0 at surface of object
Signed Distance Function
Normal Vector
Field
mmNorm
Normal Vector
Field
Relative Signed Distance Function
How can we capture all ambiguous surfaces in one function?
Unknown constant offset
We can determine the surface by finding this unknown constant offset

## Slide 114
Our Idea: Directly estimate the curvature of the object
by estimating surface normal vectors
1. Normal Field Estimation
2. Multiple Valid Surfaces
3. Single Unifying
Function
4. Isosurface
Optimization
Isosurface: Surface of constant value
Relative Signed Distance Function
Final Surface Estimate

## Slide 115
Implementation
Cardboard
Occlusion
Robot Arm
UR5e Robot Arm
TI IWR1443Boost 77GHz Radar
Intel Realsense RGB-D camera for ground truth
Measured experiments in line-of-sight and non-line-of-sight (cardboard occlusion)
Collected experiments across 61 different everyday objects
Camera (Ground-Truth)
77GHz Radar

## Slide 116
Qualitative Results
Select every voxel in SAR image above power threshold

## Slide 117
Qualitative Results

## Slide 118
Qualitative Results
1.4 cm
0.25 cm
Measure the distance from each point in the reconstruction to its nearest point in the ground truth
Measured 61 diverse everyday objects (YCB dataset)

## Slide 119
Novel Downstream Tasks
mmNorm: A paradigm shift in mmWave reconstruction
Large Scale Scenes
Shape Completion
Robotics
Augmented Reality
Indoor
Scenes
Autonomous Driving

## Slide 120
Novel Downstream Tasks
mmNorm: A paradigm shift in mmWave reconstruction
Large Scale Scenes
Shape Completion
Robotics
Augmented Reality
Indoor
Scenes
Autonomous Driving

## Slide 121
Novel Downstream Tasks
mmNorm: A paradigm shift in mmWave reconstruction
Large Scale Scenes
Shape Completion
Robotics
Augmented Reality
Indoor
Scenes
Autonomous Driving

## Slide 122
mmNorm: A paradigm shift in mmWave reconstruction
Novel Downstream Tasks
Robotics
Augmented Reality
Large Scale Scenes
Indoor
Scenes
Autonomous Driving
mmNorm Code

## Slide 123
Limitation of mmNorm: Coverage
Ground-Truth
mmNorm
Applying Vision-Based Shape-Completion
Wave-Former:
Physics-Aware Shape Completion
Missing
Surface
Poor Reconstruction

## Slide 124
Wave-Former: Physics-Aware Shape Completion
Specularity-Aware Inductive Bias:
Predict visible portions based on mmWave Physics
Incorporate :
mmWave Noise
Antenna FoVs
Feature Extractor
Physics Aware
Transformer Encoder
Physics Aware
Transformer Encoder
Joint Refinement
& Completion
Allows for training entirely on synthetic data and
testing on real world data

## Slide 125
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 126
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 127
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 128
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 129
Existing Tools
Objects
Humans
Self-Driving
Scenes
Real-World
Datasets
Open-Source Simulations
MITO – 500 images SquiggleMilli – Handheld imaging – 1500 samples | mmBody – 200k frames Milipoint – 500k frames Mmvr – 300k frames | Radatron – 500k frames Seeing through fog without seeing fog – 100k labeled pts nuScenes - 1k scenes K-Radar - | PanoRadar – 12 buildings CartoRadar – 6k Frames GRT – 1M
MITO – Ray casting based simulator GeRaF – mmWave NeRF |  |  | NVIDIA Sionna RT – Designed for mmWave Communication
Notes: Achieving camera-quality:
  Segmentation
  Classification
  6 DoF Pose Estimation
Smaller Apertures
Real-time Performance
Diffusion Models as Reconstruction Priors for Sparse Apertures
Uncertainty Aware Reconstructions
Multi-modal Fusion: RGB priors for improved reconstruction
Generalizing physical properties between different scales of mmWave imaging
Reducing Sim2Real Gap
mmWave Self-Supervised Learning Techniques

## Slide 130
Open Problems
Can we enable generalizable camera-quality mmWave perception?
Perception Tasks
Reconstruction Under Practical Constraints
Smaller Apertures
  Train Diffusion Models on reducing aperture sizes
Sparse Apertures
  Diffusion Models as Reconstruction Priors
Real-time Performance
Low Signal-to-Noise Ratio (SNR) environments
  Thicker occlusions, fewer measurements, etc
mmWave
Foundation Models
Achieving camera-quality:
  Segmentation
  Classification
  6 DoF Pose Estimation
  Material Segmentation / Estimation
Uncertainty Aware Reconstruction
Zero-shot perception
Generalizing physical insights between different scales of mmWave imaging & other domain shifts
Reducing Sim2Real Gap
mmWave Self-Supervised Learning Techniques
Multi-modal Fusion
Datasets & Benchmarking:
  Make way towards large-scale, cross device, diverse, real-world datasets
Notes: Achieving camera-quality:
  Segmentation
  Classification
  6 DoF Pose Estimation
Smaller Apertures
Real-time Performance
Diffusion Models as Reconstruction Priors for Sparse Apertures
Uncertainty Aware Reconstructions
Multi-modal Fusion: RGB priors for improved reconstruction
Generalizing physical properties between different scales of mmWave imaging
Reducing Sim2Real Gap
mmWave Self-Supervised Learning Techniques

## Slide 131
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 132
Extending Computer Vision to Hidden Objects A Tutorial on Millimeter-Wave Imaging and Reconstruction of Occluded Scenes
mmWave 101: Basics of mmWave Imaging, Limitations
State-of-the-art Reconstruction Methods
mmWave Neural Radiance Fields
Coffee Break
Vision-quality mmWave Scene Understanding
Open Problems; Tour of Existing Datasets & Tools
Hands-On Tutorial: mmWave Imaging & Reconstruction

## Slide 133
We would appreciate your feedback!
https://tinyurl.com/cvpr-mmwave
Hands-On Tutorial
https://tinyurl.com/mmwave-tutorial